Το Επιμελητήριο Φθιώτιδας ανακοινώνει στα μέλη του που έχουν αντικείμενο εργασιών «Υπηρεσίες Τηλεπικοινωνιών και Internet», ότι επιθυμεί όπως αποστείλουν στα γραφεία του Επιμελητηρίου, Όθωνος 3 – 35100 Λαμία, την οικονομική τους προσφορά (κόστος εξοπλισμού και εργασιών εγκατάστασης),  για την εγκατάσταση δωρεάν παροχής internet  στην ευρύτερη περιοχή του κέντρου της Λαμίας για τα μέλη του Επιμελητηρίου, έως την Τετάρτη 22-6-2011 και ώρα 14:00, ύστερα από σχετική απόφαση της ΔΕ.  Οι οικονομικές προσφορές θα πρέπει να είναι κλειστές και θα αξιολογηθούν από την Διοικητική Επιτροπή του Επιμελητηρίου Φθιώτιδας.

Τα προτεινόμενα τεχνικά χαρακτηριστικά του εξοπλισμού συνοψίζονται παρακάτω:

ROUTER

Router Atheros 7161 680MHz

Memory 128MB SDRAM onboard memory chip

Boot loader RouterBOOT

Data storage 512MB onboard NAND memory chip and microSD

Ethernet ports Three 10/100 Mbit/s Fast Ethernet port supporting Auto-MDI/X

Expansion 2x USB 2.0 ports, max 480Mbit throughput. Max current 2A.

MiniPCI slot Three MiniPCI Type IIIA/IIIB slots

Serial ports One DB9 RS232C asynchronous serial port

LEDs Power, NAND activity, 5 user LEDs

Extras Reset switch, Beeper.

Power options Power over Ethernet: 10..28V DC (except power over datalines)

Power jack: 10..28V DC

Power Consumption 3W without extension cards, up to 10W when using USB.

Maximum - 32W, 16W output to cards

Dimensions 10.5cm x 15cm, 137 grams

2 USB 2.0 ports για σύνδεση εξωτερικών αποθηκευτικών μέσων, 3G modems κ.α

3 microSD card slot για web proxy cache, log files, user manager and dude databases.

3 Ethernet ports and three miniPCI slots give you ample data interfaces to put the big CPU power to work.

Remote Administration

IP Addressing and Routing

Interfaces

Virtual Private Networking

Authentication, Authorization,

Accounting and Monitoring

Firewall and Quality of Service

Plug-and-Play

Network Access

System Information and Utilities

Diagnostics ToolsHigh Availability

MINI PCI

2.4GHz IEEE 802.11b/g/n standard

• Output Power of up to 25dBm @ b/g/n Band

• Support for up to 2x2 MIMO with spatial multiplexing

• Four times the throughput of 802.11g

• Atheros AR9223 chipset

• High Performance (up to 300Mbps physical data rates and 200Mbps of actual user throughput) with Low Power Consumption

• 2 X U.FL Antenna Connector

• Operating temperatures: 0C to 60C

• Power consumption MAX 2.4W

• ESD protection against +/-10kV ESD discharge on Antenna port

ΤΡΟΦΟΔΟΣΙΑ

POE 48V μεχρι 100μ

2 ANTENNAS

Frequency Range 2.3-2.7GHz

Gain 16.0-17.0dBi

Polarization Dual Linear

Cross-Pol Isolation 28dB min

Max VSWR 1.5:1

Hpol Beamwidth (6dB) 91 deg.

Vpol Beamwidth (6db) 90 deg.

Elevation Beamwidth 9 deg.

Electrical Downtilt 4 deg.

ETSI Specification EN302 326 DN2

Dimensions 700x145x79mm

Weight 3.9 kg

Windloading 160mph

1 ANTENNA

Frequency 2400-2485MHz

Gain 12dBi

Polarization Vertical

Vertical Beamwidth 9o

Horizontal Beamwidth 360o

Impedance 50 Ohm

Max Input Power 100 Watts